## Slide 2
Liquid
Chromatography
Ionization
Mass Analyzer
Detector/
Data
Collection
ESI
APCI
APPI
Triple Quadrapoles
Ion-Traps
Hybrids
Very important!
Many columns
Many solvent systems

## Slide 3
Several common modes differing by method of ion formation:
  Electrospray (ESI)
  Atmospheric Pressure Chemical Ionization (APCI)
  Atmospheric Pressure Photo-Ionization (APPI)
  New dual sources (ESI/APCI) or (APCI/APPI)

## Slide 4
It depends on the exact application.
Increasing polarity and molecular weight and thermal instability favors electrospray.
    Most drugs of abuse are highly polar and are easily analyzed using electrospray.
    High molecular weight proteins also require electrospray
Lower polarity and molecular weight favors APCI or APPI.
    Lower background, but compounds must be more thermally stable.

## Slide 5
Three Fundamental Processes:
    Production of charged droplets.
    Droplet size reduction, and fission.
    Gas phase ion formation.

## Slide 6
To MS
Orifice Plate
Curtain Plate
Drying Gas
Curtain Gas
LC
Droplet Formation
Desolvation
& Fission
Gas Phase Ion
Generation
5kV
Nebulizing
Gas

## Slide 7
A large voltage ( up to 6kV) is applied between the end of a capillary carrying the LC mobile phase and the mass spectrometer entrance.
Ions (of the same polarity) are drawn out toward the counter electrode (curtain plate) pulling the mobile phase along.
When the excess charge at the tip of the capillary overcomes surface tension, a droplet is formed.

## Slide 8
Droplet size reduction occurs by the continual repetition of two processes:
  Desolvation (evaporation of neutral solvent and volatile buffers)
  Droplet fission caused by electric repulsion between like charges.

## Slide 9
Rayleigh Jets
Columbic Repulsion =
Surface Tension
Nature 421 p128

## Slide 10
Piccole molecole volatili
EI; CI; accoppio GC e MS
Molecole polari
ESI; APCI; MALDI
Accoppiamento LCMS quando possibile

## Slide 11
SEPARAZIONE IONI NELLO SPAZIO
Settori magnetici
Quadrupoli
TOF
SEPARAZIONE
IONI NEL TEMPO
Trappole ioniche
Orbitrap
FT ICR

## Slide 12: Quadrupole Mass Ion Filter

## Slide 15
SISTEMI MASSA TANDEM ESEMPIO IL TRIPLO QUADRUPOLO

## Slide 20
MRM
SIM

## Slide 26
ION TRAP

## Slide 29: Ion Trap (trappola o gabbia ionica)

## Slide 30
Quadrupole Ion Trap

## Slide 31
Le prime trappole ioniche furono sviluppate accoppiate a sistemi GC.

## Slide 45: Time of Flight -TOF

## Slide 47
Where:
      mi = mass of analyte ion
      zi = charge on analyte ion
      E = extraction field
      ti = time-of-flight of ion
      ls = length of the source
      ld = length of the field-free drift region
      e = electronic charge (1.6022x10-19 C)

## Slide 48
TOF with reflectron

## Slide 49: Mass accuracy
Mass Error = (5 ppm)(201.1001)/106 =
 0.0010 amu
201.0991 to 201.1011 (only 1 possibility)
Sector instruments, TOF mass analyzers
How many possibilities with MA = 50 ppm?
with 100 ppm?

## Slide 50: Exact Mass Determination
Need Mass Spectrometer with a high mass accuracy – 5 ppm (sector or TOF)
C9H15NO4, FM 201.1001 (mono-isotopic)
Mass accuracy = {(Mass Error)/FM}*106
Mass Error = (5 ppm)(201.1001)/106 =
 0.0010 amu

## Slide 51: TOF Principles

## Slide 55
DETECTOR

## Slide 60
Espulsione degli ioni è assiale rispetto alla traiettoria dalla sorgente questo permette di accoppiarla ad altri analizzatori

## Slide 63: Product Ion Scan (PI)
*
*
*
*
*
*
*
*
*
*
*
*
*
*
Q1
Q2
Q3
*
*
*
*
*
DETECTOR
(CEM)
CAD GAS
Precursor Ions
Product Ions
*
Seleziono un certo m/z faccio avvenire frammentazioni
Lavoro osservando tutti gli ioni figli generati da un'unica massa iniziale per acquisire informazioni strutturali

## Slide 64
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
Q1
Q2
Q3
*
*
*
*
*
(CEM)
CAD GAS
Q1 scan
f
or a fixed mass
however more
than one molecule
may have the
same mass
Q2 Collision
Q3 Scan for another fixed
mass as a component of the
desired molecule
Precursor Ion
Product Ion
CAD
DETECTOR
MULTIPLE REACTION MONITORING (MRM)
Fisso la scansione su m/z noti di ioni iniziali noti
Se ne seleziono uno solo ho Single Ion Monitoring
SI USA PER LE ANALISI QUANTITATIVE

## Slide 65: Q-TOF Mass Analyzer
TOF
NANOSPRAY
TIP
ION
SOURCE
HEXAPOLE
COLLISION
CELL
HEXAPOLE
HEXAPOLE
QUADRUPOLE
MCP
DETECTOR
REFLECTRON
SKIMMER
PUSHER

## Slide 66
Il tacrolimus si ionizza in positivo acquistando uno ione ammonio
Std interno

## Slide 67
PRECURSOR ION SCAN
Q1
Q2
Q3
Detector
(CEM)
CAD GAS
CH
3
CH
3
CH
3
N
CH
2
CH
OR
CH
2
C
O
OC
4
H
9
CAD
H
2
C
+
CHCHCO
2
H
m/z 85
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
Acylcarnitines
*
*
*
Seleziono frammenti ottenuti da composti simili, studio composti strutturalmente correlati

## Slide 68
Advantages
  Very sensitive. (SIM)
  Good for quantitation
  Some useful MS scanning modes
Limitations
  No MSn
  Expensive
  Limited to unit mass resolution.
  Less sensitive in full scan mode.
Advantages
  Higher full scan sensitivity
  Higher mass resolution
  MSn
Limitations
  Not as good for quantitations.
  Space Charge Effects
  1/3 cut-off rule.
  Cannot perform certain MS experiments.
Triple Quadrupole
Ion Trap

## Slide 69
Q1 and Q3 are standard mass filter quadrupoles.
  The can scan masses sequentially (e.g. 50 to 500 amu)
  The can be used to select a single mass.
Q2 is an RF only quadrupole that is in a gas filled chamber.
  Q2 is the “collision cell” where mass fragmentation occurs.
  Q2 does not filter ions. It accepts all ion sent to it by Q1 and passes all ions formed by collision to Q3 to be sorted.
Q1
Q2
Q3
Q0
RF only Collision Cell
Scanning
RF/DC
Scanning
RF/DC
RF only

## Slide 70
Ions fill the space between a ring electrode and a pair of end-cap electrodes.
Mass analysis and fragmentation occur in the same space.