## Slide 1: NMR e analisi farmaceutiche
Identificazione composti 1D e 2D NMR
Quantitative NMR?
Diffusion order spectroscopy (DOSY)
NMR applications in metabolomics, etc

## Slide 3
Energy and spectroscopy: Where is NMR?
Very low energy in the process…
Wavelength >108

## Slide 5: NMR “the physical technique that has changed chemistry”
Structure elucidation (pure compounds)
  Organic synthesis
  Natural product isolation
  Identification of adducts/metabolites both of chemical/biochemical reactions

## Slide 6
NMR: basic 1D and 2D
Q: How many spectroscopists does it take to prepare a sample?
A: None. That's what chemists are for. (very old)
Product Operator Formalism: ...it would be better for chemistry if there were no mathematicians on the earth

## Slide 7
What is a crio magnet?
Why the instrument must be filled with liquid N2 and liquid He?
http://www.jeolusa.com/SERVICESUPPORT/ApplicationsResources/AnalyticalInstruments/NMRMagnetDestruction/tabid/390/Default.aspx

## Slide 8
NMR hardware:
Crio-magnet
Radiofrequences generator
Radiofrequence receiver

## Slide 9
NUCLEAR spin
This is a fundamental property of nuclei. Nucei are charged particles moving. They rotate and this rotation is generating an angular or magnetic“moment” P (that is spin)
P =
P : vector oriented due to rotation, e il Number of spin I is an index of the intensity of the rotation
I= 0, ½, 1, up to 6.

## Slide 10
Each nucleus is a small magnet and in its rotation we can measure a angular moment direct proportional to P and with same direction. Only two directions (for I = ½) are possible.
 =  P
giromagnetic ratio

+
+

 = /P
ANGULAR MOMENTUM

## Slide 11
Zeeman splitting

## Slide 12
Three opportunities:
I=0 no magnetic momentum 12C o 16O. NO NMR signal !
I=1/2 spheres, 1H, 13C, 19F, ecc.
I>1/2 non spheric charge particles (Deuterium 14N etc.)

## Slide 13
Just for having an idea: two different nuclei.
1H
2H, 14N

## Slide 14
B0 increasing
+ 1/2
- 1/2
Degeneri a
B0 = 0
Δ E is related to B0 and 

## Slide 15
When there is B nuclei precess with speed w.
N
S

h
Se  spin inversion
NMR
frequency
400 - 600 MHz

## Slide 16



Bo
 è una costante per ciascun nucleo (H, C, N, etc)
E = h
Giromagnetic ratio
Ext field
Frequency of radiation that is able to perform a transition
Larmor frequency
Signal is when a nucleus has absorbed the proper energy that allows…

## Slide 17
 = E/h
If I = ½, m is +½ o –½, so:
E=h
 giromagnetic ratio and h Plank constant
 h B0
E=

 B0
 =


## Slide 18
Rf pulse
Magetization
Relaxation and resonance

## Slide 19
E=h
 B0
 =

This product is a constant
This means that when I use small time for frequency emission I’m emitting frequency intervals.
So with one rf pulse I gave to the sample all the possible frequencies (for H as example).

## Slide 20
SPECTRUM

## Slide 21
A large number
of frequencies
RF broad band
Single pulse i give all frequencies
N
S
1
2
3
1 ..... n
impulse FT-NMR

## Slide 22
( relaxation
FREE INDUCTION DECAY
Each atom generate its own frequency and i collect all this FID mixed.
Fourier transform the graph from time domain to frequency domain (clear?=)

## Slide 23
Time domain
1 + 2 + 3 + ......
time

## Slide 24
Making a FID becoming a NMR spectrum
unreadable
1 + 2 + 3 + ......
FT-NMR
frequencies
Time non readable
frequencies
Mixed frequencies
FID
NMR spectrum
Fourier Transform

## Slide 25
RELAXATION
After the pulse our nuclei will come back to initial situation
Spin lattice relaxation (T1): coming back from excited state to fundamental.
The relaxation time T1 represents the "lifetime" of the first order rate process that returns the magnetization to the Boltzman equilibrium along the +Z axis.
T2 represents the lifetime of the signal in the transverse plane (XY plane) and it is this relaxation time that is responsible for the line width. The "true" line width on an NMR signal depends on the relaxation time T2 (line width at half-height=1/T2).

## Slide 26
Reading NMR spectrum:
Chemical shift
Integral value
Molteplicity signal shape?

## Slide 27



Bo
 è una costante per ciascun nucleo (H, C, N, etc)
E = h
Giromagnetic ratio
Ext field
Frequency of radiation that is able to perform a transition
Larmor frequency
Signal is when a nucleus has absorbed the proper energy that allows…

## Slide 28
The frequency is a function of:
-Nucleus
-external field.
But each atom is rounded by other atoms that induce modification in its magnetic situation
Breal=B0-Bi
Shielding or de-shielding effects due to induced field direction.

## Slide 29
Different chemical situations generated different resonance frequence
B= B0 (1-)
Electrons due to magnetic field are forced to rotate and they create further magnetic field
The magnetic field is opposite to external one in the central part of the orbital while is addictive in the external part. As much the nucleus is near to central part of orbital it will be shielded by bond electrons

## Slide 30
Ppm scale
Ppm scale is not depending on magnet strenght!!!!!
=
[j]-[ref]
[ref]
106
why TMS?
12 shielded identical protons
soluble
volatile
reference TMS
Spectrometer frequency

## Slide 31
Ppm scale

0
2
4
6
8
10
CH2Ar
CH2NR2
CH2S
C C-H
C=C-CH2
CH2-C-
CH2F
CH2Cl
CH2Br
CH2I
CH2O
CH2NO2
deshielded
shielded
0
30
90
200
120
13C
1H

## Slide 32
Electronic density is the main discriminant
-

C
H
Cl
Electron attractive group
-

compound CH3X
X
electronegativity of X
Chemical shift 
CH3F CH3OH CH3Cl CH3Br CH3I CH4 (CH3)4Si
F O Cl Br I H Si
4.0 3.5 3.1 2.8 2.5 2.1 1.8
4.26 3.40 3.05 2.68 2.16 0.23 0
TMS
deshielded

## Slide 33
Sp2 carbons has deshielded chemical shifts (compared to sp3),  5-6. due to  electrons.
C=C
H
H
H
H
BO
I protoni sono deschermati
Linee di forza del campo magnetico indotto
Chemical shift anysotropy

## Slide 34
Bo
H
H
C
C
Shielded H
B induced
The symmetry of CC bond create their shielded situation.

## Slide 35
electrons 
B0
deshielded
H
H
Aromatics: ring current
Line of magnetic field of electrons

## Slide 36
CHEMICAL SHIFTS (ppm)
1.0 - 4.0
R-C C-H 1.7 - 2.7
R-CH3 0.7 - 1.3
R-C=C-C-H 1.6 - 2.6
R-C-C-H 2.1 - 2.4
O
O
RO-C-C-H 2.1 - 2.5
O
HO-C-C-H 2.1 - 2.5
N C-C-H 2.1 - 3.0
R-C C-C-H 2.1 - 3.0
C-H 2.3 - 2.7
R-N-C-H 2.2 - 2.9
R-S-C-H 2.0 - 3.0
I-C-H 2.0 - 4.0
Br-C-H 2.7 - 4.1
Cl-C-H 3.1 - 4.1
RO-C-H 3.2 - 3.8
HO-C-H 3.2 - 3.8
R-C-O-C-H 3.5 - 4.8
O
R-C=C-H
H
6.5 - 8.0
R-C-H
O
9.0 - 10.0
R-C-O-H
O
11.0 - 12.0
O2N-C-H 4.1 - 4.3
F-C-H 4.2 - 4.8
R3CH 1.4 - 1.7
R-CH2-R 1.2 - 1.4
4.5 - 6.5
R-N-H 0.5 - 4.0 Ar-N-H 3.0 - 5.0 R-S-H
R-O-H 0.5 - 5.0 Ar-O-H 4.0 - 7.0
R-C-N-H
O
5.0 - 9.0

## Slide 37
Reading NMR spectrum:
Chemical shift
Integral value
Molteplicity signal shape?

## Slide 38
HX and HA, have mutual influence. If HA is  o : HX is shielded in the first, and deshielded in the second case. For this reason, HX near to HA has different resonances if is experiment HA as  or .
HA and HX. HA can have spin  or  :
What happens when nuclei are near?

## Slide 39
C
C
H
H
C
C
H
H
A
A
Bo
HA frequency is changed by spin state of nearby atoms
50 % di molecole
Allineato con B0
Opposto a Bo
+1/2
-1/2
50 % di molecole
DOUBLET

## Slide 40
J.= difference of frequencies of the two part of doublet
The chemical shift is in the center
Copuling constant

## Slide 41
First order spin systems
A and X copuling. If they have different chemical shift we have doublets
Roof effect when difference is less
>>J
AX

## Slide 42
A2X
CHCl2–CH2Cl

## Slide 43
A3X2
C
C
H
H
H
H
H
C
C
H
H
H
H
H

## Slide 44
n+1 rule
Multiplicity of a certain signal

## Slide 45
( x = y )
( x = y )

## Slide 46
1 2 1
1
1 1
1 3 3 1
1 4 6 4 1
1 5 10 10 5 1
1 6 15 20 15 6 1
1 7 21 35 35 21 7 1
singlet
doublet
triplet
quartet
quintet
sextet
heptet
8…
Intensity of multiplet lines
Il triangolo di Tartaglia

## Slide 47
Eccezioni alla regola N+1
IMPORTANT !
Symmetric protons do not copule
No copuling if x=y
1)
2)
Equivalent for free rotation
or

## Slide 48
Vicinal copuling.small for gaughe (=60°), higher for anti (=180°).
J = J0 cos2f for 0 <  < 90
J = J180 cos2f for 90 < < 180
Karplus law

## Slide 49
And what about 3J.
3J
2J
2J
copuling constants: more descriptives than chemical shift!
H on C sp3: J  10-14 Hz
H on C sp2: J  1-3 Hz

## Slide 50
3J
Single bond free rotation: J  7 Hz
Single bond fixed angle : Karplus law
6 member chains single bondchair shape: Jax,ax  10 Hz
Jax,eq  3 Hz
Jeq,eq  3 Hz
5 member rings single bond : J  5 Hz (cis,trans)
Double bonds: Jcis  7-11 Hz
Jtrans  14-17 Hz
Aromatic rings 6 atoms: Jorto  7-9 Hz
Aromatic rings 5 atoms: Jorto  3-5 Hz
3J.

## Slide 51
Allilic (4J: CH-C=CH): J  0-2 Hz
Omoallilic (5J: CH-C=C-CH): J  0-2 Hz
Aromatic rings: Jmeta  1-3 Hz
Jpara  0-1 Hz
W: 4J  0-7 Hz
long-range copulings constants.

## Slide 52
Equivalent protons
Examples
symmetry
free rotations

## Slide 54
noise
signal
R ≈
etc.
1° impulso
2° impulso
nth pulse
Aumenta S ≈ N
S/R ratio is increased summing several spectra

## Slide 57
NMR-Bidimensionale
Gli spettri protonici e 13C sono grafici a due dimensioni che riportano il c. s in funzione dell’intensità del segnale. Tuttavia li si definisce esperimenti monodimensionali in quanto esiste una sola variabile indipendente rappresentata dalla frequenza che deriva dall’ FT del FID. Nelle tecniche monodimensionali classiche la sequenza degli eventi è la seguente:
Nelle tecniche bidimensionali si introduce, dopo l’impulso e prima dell’acquisizione un periodo di evoluzione variabile t1. Ciascun FID sarà quindi funzioni di due variabili di tempo t1 e t2

## Slide 58: Bidimensional measuraments

## Slide 59
In 2D NMR we introduce a variable t1 so we get a series of different FID evolving both in t2 and t1.
Monodimensional experiment the FID is evolving in t2 time scale

## Slide 61
If we merge all the FID we get 2D spectrum. The FT of the FID get to spectra changing their intensity in oscillating mode.

## Slide 62
The FIDs are FT in two different time domains dephased of 90°. So we will have two dimensions 1 and 2

## Slide 63
Omonuclear
2D-COSY (1H-1H copuling)
HOHAHA-TOCSY (1H-1H copuling)
NOESY (1H-1H dipolar interactions)
Eteronuclear
HMQC, HSQC (1H-13C, 1J)
HMBC (1H-13C long-range, 2J, 3J)
Most common 2D experiments